## Slide 1: mSWAT: Hardware Fault Detection and Diagnosis for Multicore Systems*
Siva Kumar Sastry Hari, Man-Lap (Alex) Li,
Pradeep Ramachandran, Byn Choi, Sarita Adve
Department of Computer Science
University of Illinois at Urbana-Champaign
swat@cs.uiuc.edu
*To appear in MICRO’09

## Slide 2: Motivation
Goal
  Hardware resilience with low overhead
Previous Work
  SWAT – low-cost fault detection and diagnosis
  For single-threaded workloads
This work
  Fault detection and diagnosis for multithreaded apps
Notes: The goal of this project is to provide high hardware reliability with low overehad in terms of area, perf and power.
Since the reliability probelm is becoming pervasive across different markets, we need a low cost reliability solution.
Previously we propsed SWAT that detects faults with low overhead symptom detectors. And it diagnoses faults at
microarchitecture level
With the advent of multicore era, multithreaded applications are becoming common. Therefore, in this work we focus
on fault detection and diagnosis for multithreaded applications

## Slide 3: SWAT Background
SWAT Observations
Need handle only hardware faults that propagate to software
Fault-free case remains common, must be optimized
SWAT Approach
Watch for software anomalies (symptoms)
    Zero to low overhead “always-on” monitors

## Slide 4: SWAT Framework Components
Fault
Error
Symptom
detected
Recovery
Diagnosis
Repair
Checkpoint
Checkpoint
Detectors with simple hardware [ASPLOS’08]
Detectors with compiler support [DSN’08]
µarch-level Fault Diagnosis (TBFD) [DSN’08]

## Slide 5: Challenge
Fault
Error
Symptom
detected
Recovery
Diagnosis
Repair
Checkpoint
Checkpoint
Detectors with simple hardware
Detectors with compiler support
µarch-level Fault Diagnosis (TBFD)
Shown to work well for single-threaded apps
Does SWAT approach work on multithreaded apps?

## Slide 6: Multithreaded Applications
Multithreaded apps share data among threads
Symptom causing core may not be faulty
Need to diagnose faulty core
Symptom Detection
on a fault-free core
Core 2
Fault
Core 1
Store
Memory
Load

## Slide 7: mSWAT Fault Detection
SWAT Detectors
  Fatal traps
    Division by Zero, RED State, etc.
  Hangs detected
  High OS activity
New symptom: Panic detected when kernel panics
Low-cost SWAT-like detectors provide high coverage

## Slide 8: Fault Diagnosis
After detection, invoke diagnosis to identify the faulty core
Replay fault activating execution
  Look for divergence among the two executions
  Identify transients or permanent or software fault
Challenge
  Faulty core is unkown
  No good core known for comparison

## Slide 9: Diagnosis for Multithreaded Apps
Simple implementation – One spare core
  Not Scalable, requires N full-system deterministic replays
  Requires a spare core
  Single point of failure
C1
S
C2
C3
Symptom Detected
C1
S
C2
C3
No Symptom Detected
C1
S
C2
C3
Symptom Detected
Faulty core
is C2

## Slide 10: mSWAT Diagnosis - Key Ideas
Challenges
Multithreaded applications
Full-system deterministic replay
No known
good core
Isolated deterministic replay
Emulated TMR
Key Ideas
TA
TB
TC
TD
TA
TA
TB
TC
TD
TA
A B C D
TA
A B C D

## Slide 11: mSWAT Diagnosis - Key Ideas
Challenges
Multithreaded applications
Full-system deterministic replay
No known
good core
Isolated deterministic replay
Emulated TMR
Key Ideas
TA
TB
TC
TD
TA
TA
TB
TC
TD
A B C D
A B C D
TD
TA
TB
TC
TC
TD
TA
TB

## Slide 12: Multicore Fault Diagnosis Algorithm
Symptom
detected
Capture fault
activating trace
Re-execute
Captured trace
Diagnosis
TA
TB
TC
TD
A B C D
Example

## Slide 13: Multicore Fault Diagnosis Algorithm
Symptom
detected
Capture fault
activating trace
Re-execute
Captured trace
Diagnosis
TA
TB
TC
TD
A B C D
A B C D
Example

## Slide 14: Multicore Fault Diagnosis Algorithm
Symptom
detected
Capture fault
activating trace
Re-execute
Captured trace
Faulty
core
Look for divergence
Diagnosis
TA
TB
TC
TD
A B C D
TD
TA
TB
TC
A B C D
Divergence
Example
TA
A B C D
No Divergence
Faulty core is B

## Slide 15: mSWAT Summary and Advantages
Detection
  Coverage over 98% with low SDC rate of 0.2%
Diagnosis
  High diagnosability over 95% with low diagnosis latency
  Scalable - maximum of 3 replays for any system
  Firmware based replay reduces hw overhead

## Slide 16: Thank you