## Slide 1
Relyzer: Exploiting Application-level Fault Equivalence to Analyze Application Resiliency to Transient Faults
Siva Hari1, Sarita Adve1, Helia Naeimi2, Pradeep Ramachandran2
1 University of Illinois at Urbana-Champaign,
2 Intel Corporation
swat@cs.illinois.edu

## Slide 2: Motivation
Hardware reliability is a major challenge
  Transient (soft) errors are a major problem
  Need in-field low-cost reliability solution
Traditional redundancy based solutions are expensive
Alternative: Treat s/w anomalies as symptoms of h/w faults
  Detect faults using low-cost software symptom monitors
  Diagnosis, recovery more complex, but infrequent
Efficacy depends heavily on application
How to evaluate application-level resiliency?
Soft Error
Notes: As technology scales, the smaller devices become increasingly unreliable making hardware reliability a major challenge. Transient errors form a major source of the infield failures. Hence there is a need for in-field low-cost reliability solutions.
Traditional redundancy based solutions are becoming expensive in area, performance, and power.
As an alternative, recently, researchers have proposed solutions that are software driven. These solutions treat anomalous software behavior as symptoms of hardware faults. They deploy low-cost symptom monitors to detect faults in the system. In the infrequent case of fault detection, more sophisticated diagnosis and recovery module are invoked.
Clearly the efficacy of such an approach depends heavily on the application that is being executed, i.e., when in the application the fault occurs and how it propagates through the application execution. Hence the ability to evaluate and understand the resiliency of an application is important. This talk describes a tool that provides such an understanding.

## Slide 3: Fault Outcomes
APPLICATION
.
.
.
Output
Fault-free
execution

## Slide 4: Fault Outcomes
APPLICATION
.
.
.
Output
Fault-free
execution
Masked
APPLICATION
.
.
.
Output
Transient Fault
e.g., bit 4 in R1
Faulty executions

## Slide 5: Fault Outcomes
APPLICATION
.
.
.
Output
Fault-free
execution
Faulty executions
Masked
APPLICATION
.
.
.
Output
APPLICATION
.
.
.
Output
Symptom detectors (SWAT):
Fatal traps, assertion violations, etc.
Symptom of Fault
Detection
Transient fault
again in bit 4 in R1

## Slide 6: Fault Outcomes
APPLICATION
.
.
.
Output
Fault-free
execution
Masked
APPLICATION
.
.
.
Output
APPLICATION
.
.
.
Output
Symptom of Fault
APPLICATION
.
.
.
Output
X
Detection
SDC
Faulty executions
Silent Data
Corruption (SDC)

## Slide 7: Fault Outcomes
APPLICATION
.
.
.
Output
Fault-free
execution
Masked
APPLICATION
.
.
.
Output
APPLICATION
.
.
.
Output
Symptom of Fault
APPLICATION
.
.
.
Output
Detection
SDC
Faulty executions
Goal: Lower SDC rate to zero

## Slide 8: Silent Data Corruptions
APPLICATION
.
.
.
Output
SDC
Symptom detectors are effective, BUT
  SDC rate is still >0%
Two key challenges
  Which application fault sites cause SDCs?
  How to convert SDCs to detections?

## Slide 9: Silent Data Corruptions
APPLICATION
.
.
.
Output
SDC
Symptom detectors are effective, BUT
  SDC rate is still >0%
Two key challenges
  Which application fault sites cause SDCs?
    Relyzer lists SDC sites
  How to convert SDCs to detections?
    Relyzer guides detectors [DSN’12]

## Slide 10: Evaluating Application-Level Resiliency
Statistical Fault Injection
Injections in few sites
Cannot find all SDC sites
APPLICATION
.
.
.
Output

## Slide 11: Evaluating Application-Level Resiliency
APPLICATION
.
.
.
Output
Relyzer: Analyze all app fault sites with few injections
Statistical Fault Injection
Injections in few sites
Cannot find all SDC sites
Ideal Injection
Injections in ALL sites
Find ALL SDC sites
Goal:
Find ALL SDC sites
injections in few sites
with

## Slide 12: Relyzer Approach
APPLICATION
.
.
.
Output
Prune fault sites
Show application-level fault equivalence
Predict fault outcomes without injections
Detailed injections for remaining faults
Equivalence
Classes
Pilots

## Slide 13: Contributions
Relyzer: A tool for complete application resiliency analysis
Developed novel fault pruning techniques
  3 to 6 orders of magnitude fewer injections for most apps
  99.78% app fault sites pruned
    Only 0.04% represent 99% of all fault sites
Can identify all potential SDC causing fault sites
APPLICATION
.
.
.
Output
APPLICATION
.
.
.
Output

## Slide 14: Outline
Motivation
Pruning Techniques
Methodology and Results
Conclusions and Ongoing Work

## Slide 15: Outline
Motivation
Pruning Techniques
  Application-level fault equivalence
  Predictable faults
Methodology and Results
Conclusions and Ongoing Work

## Slide 16: Outline
Motivation
Pruning Techniques
  Application-level fault equivalence
    Control flow equivalence
    Store equivalence
    Definition to first use equivalence
  Predictable faults
Methodology and Results
Conclusions and Ongoing Work

## Slide 17: Control Flow Equivalence
  Insight: Faults flowing through similar control paths may behave similarly
CFG
X

## Slide 18: Control Flow Equivalence
  Insight: Faults flowing through similar control paths may behave similarly
CFG
X
X
X
X
X
X

## Slide 19: Control Flow Equivalence
  Insight: Faults flowing through similar control paths may behave similarly
CFG
Faults in X that take paths behave similarly
Heuristic: Use direction of next 5 branches
X

## Slide 20: Store Equivalence
Insight: Faults in stores may be similar if stored values are used similarly
Heuristic to determine similar use of values:
  Same number of loads use the value
  Loads are from same PCs
Store
Memory
PC1
PC2
Load
Load
Store
PC1
PC2
Load
Load
Instance 1
Instance 2
PC
PC

## Slide 21: Def to First-Use Equivalence
Fault in first use is equivalent to fault in def  prune def
  r1 = r2 + r3
  r4 = r1 + r5
  …
If there is no first use, then def is dead  prune def
Def
First use

## Slide 22: Pruning Predictable Faults
Prune out-of-bounds accesses
  Detected by symptom detectors
  Memory addresses not in &
Boundaries obtained by profiling
Reserved
Stack
Reserved
Heap
Data
Text
SPARC Address Space Layout
0x0
0x100000000
0x80100000000
0xfffff7ff00000000
0xffffffffffbf0000

## Slide 23: Methodology
Pruning
  12 applications (from SPEC 2006, Parsec, and Splash 2)
Fault model
  Where (hardware) and when (application) to inject transient faults
  Where: Hardware fault sites
    Faults in integer arch registers
    Faults in output latch of address generation unit
  When: Every dynamic instruction that uses these units

## Slide 24: Pruning Results
99.78% of fault sites are pruned
3 to 6 orders of magnitude pruning for most applications
  For mcf, two store instructions observed low pruning (of 20%)
Overall 0.004% fault sites represent 99% of total fault sites
Chart: % of all fault sites
| Blackscholes | Fluidanimate | Streamcluster | Swaptions | FFT | LU | Ocean | Water | GCC | Libquantum | Mcf | Omnet++ | Total | Parsec 2.1 | Splash 2 | SPEC 2006 |
Remaining | 0.99996 | 0.9991 | 0.99992 | 0.99999 | 0.99999 | 0.99997 | 0.99987 | 0.99994 | 0.99875 | 0.99985 | 0.99427 | 0.99998 | 0.99781

## Slide 25: Contribution of Pruning Techniques
Both equivalence and prediction based techniques are effective
Chart: Average
| Average | 26.54% | 14.86% | 10.36% | 48.25%
Prediction-based | 0.26535
Def-Use | 0.14856
Store | 0.10356
Control | 0.48253

## Slide 26: Methodology: Validating Pruning Techniques
PILOTS
SAMPLE
Validation for Control and Store equivalence pruning
APPLICATION
.
.
.
Output
Compute Prediction Rate
Equivalence
Classes

## Slide 27: Validating Pruning Techniques
Validated control and store equivalence
  >2M injections for randomly selected pilots, samples from equivalent set
96% combined accuracy (including fully accurate prediction-based pruning)
99% confidence interval with <5% error
Chart: Average Prediction Rate
| Reg - Control | Reg - Store | Agen - Control | Agen - Store | Combined
Average | 0.95682 | 0.95395 | 0.94523 | 0.9264 | 0.96026

## Slide 28: Conclusions and Ongoing Work
Relyzer: Novel fault pruning for application resiliency analysis
  3 to 6 orders of magnitude fewer injections for most apps
    99.78% of fault sites pruned
      Only 0.004% represent 99% of all fault sites
    Average 96% validation
Can list all SDC prone instructions and fault propagation path
  Guides low-cost detectors
  Ongoing work (to appear in DSN’12)
    Understand application properties responsible for SDCs
    Devise (automate) low-cost app-level detectors
    Quantifiable resilience vs. performance

## Slide 29
Relyzer:
Exploiting Application-level Fault Equivalence to Analyze Application Resiliency to Transient Faults
Siva Hari1, Sarita Adve1, Helia Naeimi2, Pradeep Ramachandran2
1 University of Illinois at Urbana-Champaign,
2 Intel Corporation
swat@cs.illinois.edu