## Slide 1
Low-cost Program-level Detectors for Reducing Silent Data Corruptions
Siva Hari†, Sarita Adve†, and Helia Naeimi‡
†University of Illinois at Urbana-Champaign,
‡Intel Corporation
swat@cs.illinois.edu

## Slide 2: Motivation
Hardware reliability is a challenge
  Transient (soft) errors are a major problem
Soft Error
Redundancy
Overhead (perf., power, area)
How?
Tunable
reliability
Reliability
Very high
reliability at low-cost
Symptom-based
Detect errors using
symptom monitors
Fatal Traps
Kernel Panic
App Abort
Goals:
Full reliability at low-cost
Tunable reliability vs. overhead

## Slide 3: Fault Outcomes
APPLICATION
.
.
.
Output
Symptom of Fault
Transient
fault
APPLICATION
.
.
.
Output
Transient fault
(e.g., bit 4 in R2)
APPLICATION
.
.
.
Output
Symptom detectors (SWAT):
Fatal traps, kernel panic, etc.
Output
Masked
Silent Data Corruption
(SDC)
Transient
fault
Detection
How to convert SDCs to detections?

## Slide 4: SDCs to Detections
Add new detectors in error propagation path?
  SDC coverage: Fraction of all SDCs converted to detections
Will it be low-cost?
APPLICATION
.
.
.
Output
Output
Silent Data Corruption
(SDC)
APPLICATION
.
.
Error Detection
Error Detectors

## Slide 5: Key Challenges
What to
protect?
SDC
-
causing fault sites
Identified using
Relyzer
[ASPLOS’12]
How to
Protect?
Low
-
cost Detectors
Where to place?
Many errors propagate to
few program values
What detectors?
Program
-
level properties
tests
Uncovered
fault
-
sites?
Selective instruction
-
level duplication

## Slide 6: Contributions
Discovered common program properties around most SDC-causing sites
Devised low-cost program-level detectors
  Average SDC reduction of 84%
  Average execution overhead 10%
New detectors + selective duplication = Tunable resiliency at low-cost
  Found near optimal detectors for any SDC target
  Lower cost than pure redundancy for all SDC targets
    E.g., 12% vs. 30% @ 90% SDC reduction

## Slide 7: Outline
Motivation and introduction
Categorizing and protecting SDC-causing sites
Tunable resilience vs. overhead
Methodology
Results
Conclusions

## Slide 8: Outline
Motivation and introduction
Categorizing and protecting SDC-causing sites
  Loop incrementalization
  Registers with long life
  Application-specific behavior
Tunable resilience vs. overhead
Methodology
Results
Conclusions

## Slide 9: Insights
Identify where to place the detectors and what detectors to use
Placement of detectors (where)
  Many errors propagate to few program values
    End of loops and function calls
Detectors (what)
  Test program-level properties
    E.g., comparing similar computations and checking value equality
Fault model
  Single bit flips in integer arch. registers

## Slide 10: Loop Incrementalization
rA = base addr. of a
rB = base addr. of b
L: load r1 ← [rA]
. . .
load r2 ← [rB]
. . .
store r3 → [rA]
. . .
add rA = rA + 0x8
add rB = rB + 0x8
add i = i + 1
branch (i<n) L
Array a, b;
For (i=0 to n) {
. . .
a[i] = b[i] + a[i]
. . .
}
C Code
ASM Code

## Slide 11: Loop Incrementalization
rA = base addr. of a
rB = base addr. of b
L: load r1 ← [rA]
. . .
load r2 ← [rB]
. . .
store r3 → [rA]
. . .
add rA = rA + 0x8
add rB = rB + 0x8
add i = i + 1
branch (i<n) L
Array a, b;
For (i=0 to n) {
. . .
a[i] = b[i] + a[i]
. . .
}
C Code
ASM Code
Where: Errors from all iterations propagate here in few quantities
What: Property checks on rA, rB, and i
Diff in rA = Diff in rB
Diff in rA = 8 Diff in i
Collect initial values of rA, rB, and i
SDC-hot app sites
No loss in coverage - lossless

## Slide 12: Registers with Long Life
Some long lived registers are prone to SDCs
For detection
  Duplicate the register value at its definition
  Compare its value at the end of its life
No loss in coverage - lossless
Life
time
R1 definition
Copy
Use 1
Compare
Use 2
Use n
.
.
.

## Slide 13: Application-Specific Behavior
Exponential function
  Where: End of every function invocation
  What: Re-execution or inverse function (log)
  Periodic test on accumulated quantities
  Accumulate input and output with and
Some coverage may be compromised – lossy
exp
exp
few
s

## Slide 14: Application-Specific Behavior (Contd.)
Bit Reverse function
  Where: End of function
  What: Challenge – re-execution?
  Approach: Parity of in & out should match
Other detectors: Range checks
Some coverage may be compromised – lossy
Bit Reverse
Compare
Parity
Parity

## Slide 15: Tunable Resiliency vs. Overhead
What if our detectors do not cover all SDC-causing sites?
  Use selective instruction-level redundancy
What if our low-overhead is still not tolerable but lower resiliency is?
  Tunable resiliency vs. overhead

## Slide 16: Identifying Near Optimal Detectors: Naïve Approach
Bag of detectors
SDC coverage
SFI
50%
Example: Target SDC coverage = 60%
Sample 1
Overhead = 10%
Sample 2
Overhead = 20%
SFI
65%
Tedious and time consuming

## Slide 17: Identifying Near Optimal Detectors: Our Approach
Bag of detectors
Selected Detectors
SDC Covg.= X%
Overhead = Y%
Detector
1. Set attributes, enabled by Relyzer [ASPLOS’12]
2. Dynamic programming
Constraint: Total SDC covg. ≥ 60%
Objective: Minimize overhead
Overhead = 9%
Obtained SDC coverage vs. Performance trade-off curves

## Slide 18: Methodology
Six applications from SPEC 2006, Parsec, and SPLASH2
Fault model: single bit flips in int arch registers at every dynamic instr
Ran Relyzer, obtained SDC-causing sites, examined them manually
Our detectors
  Implemented in architecture simulator
  Overhead estimation: Num assembly instrns needed
Selective redundancy
  Overhead estimation: 1 extra instrn for every uncovered instrn
Lossy detectors’ coverage
  Statistical fault injections (10,000)

## Slide 19: Categorization of SDC-causing Sites
Categorized >88% SDC-causing sites
Added Lossy
Detectors
Chart: % SDCs
| Blackscholes | FFT | Libquantum | LU | Swaptions | Water
Loop Incrementalization | 11.8789 | 46.8113 | 41.9375 | 81.5356 | 4.5703 | 28.6771
Registers with long life | 10.5795 | 6.9234 | 48.8608 | 11.2881 | 0.73993 | 14.3507
App specific | 76.4548 | 34.7807 | 0 | 0 | 91.4624 | 46.7264
Uncovered | 1.0868 | 11.4845 | 9.2017 | 7.1762 | 3.2274 | 10.2458
Added Lossless Detectors

## Slide 20: SDC coverage
84% average SDC coverage (67% - 92%)
Chart: SDC Coverage
| Blackscholes | FFT | Libquantum | LU | Swaptions | Water | Average
Lossless | 0.22458 | 0.53735 | 0.90798 | 0.92824 | 0.053102 | 0.43028 | 0.51359
Lossy | 0.64408 | 0.25221 | 0 | 0 | 0.61653 | 0.42931 | 0.32369

## Slide 21: SDC coverage
Chart: SDC Coverage
| Blackscholes | FFT | Libquantum | LU | Swaptions | Water | Average
Lossless | 0.22458 | 0.53735 | 0.90798 | 0.92824 | 0.053102 | 0.43028 | 0.51359
Lossy | 0.64408 | 0.25221 | 0 | 0 | 0.61653 | 0.42931 | 0.32369
84% average SDC coverage (67% - 92%)

## Slide 22: Execution Overhead
10% average overhead (0.1% - 18%)
Chart: Execution Overhead
| Blackscholes | FFT | Libquantum | LU | Swaptions | Water | Average
Lossless | 1.6586e-06 | 0.077648 | 0.00079089 | 0.12571 | 0.0448 | 0.053963 | 0.050486
Lossy | 0.17627 | 0.084192 | 1e-08 | 1e-08 | 0.010426 | 0.035133 | 0.051003

## Slide 23: Execution Overhead
10% average overhead (0.1% - 18%)
Chart: Execution Overhead
| Blackscholes | FFT | Libquantum | LU | Swaptions | Water | Average
Lossless | 1.6586e-06 | 0.077648 | 0.00079089 | 0.12571 | 0.0448 | 0.053963 | 0.050486
Lossy | 0.17627 | 0.084192 | 1e-08 | 1e-08 | 0.010426 | 0.035133 | 0.051003

## Slide 24: SDC Coverage vs. Overhead Curve
Consistently better over pure (selective) instruction-level duplication
Our detectors + Redundancy
Pure Redundancy
Chart: SDC Coverage
18%
90%
24%
99%

## Slide 25: Conclusions
Reduction in SDCs is crucial for low-cost reliability
Discovered common program properties around most SDC-causing sites
Devised low-cost program-level detectors
  84% avg. SDC coverage at 10% avg. cost
New detectors + selective duplication = Tunable resiliency at low-cost
  Found near optimal detectors for any SDC target
  Lower cost than pure redundancy for all SDC targets
Future directions
  More applications and fault models
  Automating detectors’ placement and derivation