## Slide 1
Eliminating Silent Data Corruptions
caused by Soft-Errors
Siva Hari,
Sarita Adve, Helia Naeimi, Pradeep Ramachandran,
University of Illinois at Urbana-Champaign,
shari2@illinois.edu

## Slide 2: Technology Scaling and Reliability Challenges
Nanometers
Increase (X)
Our Focus
*Source: Inter-Agency Workshop on HPC Resilience at Extreme Scale
hosted by NSA Advanced Computing Systems, DOE/SC, and DOE/NNSA, Feb 2012
Chart: 
| 2008 | 2010 | 2012 | 2014 | 2016 | 2018 | 2020
Technology | 45 | 32 | 22 | 14 | 10 | 7 | 5
Chart: 
| 2008 | 2010 | 2012 | 2014 | 2016 | 2018 | 2020
Technology | 45 | 32 | 22 | 14 | 10 | 7 | 5
Reliability challenges | 0 | 4 | 6.3 | 9.6 | 14.9 | 24.6 | 42.9
Chart: 
| 2008 | 2010 | 2012 | 2014 | 2016 | 2018 | 2020
Technology | 45 | 32 | 22 | 14 | 10 | 7 | 5
Reliability challenges | 0 | 4 | 6.3 | 9.6 | 14.9 | 24.6 | 42.9
SER Mem | 0 | 1 | 1 | 1 | 1 | 1 | 1
SER Logic | 0 | 1 | 2 | 4 | 8 | 16 | 32
Variability | 0 | 1 | 1.3 | 1.6 | 1.9 | 2.1 | 2.4
Aging | 0 | 1 | 2 | 3 | 4 | 5.5 | 7.5
Notes: With technology scaling, the increasingly smaller devices improve performance and power-efficiency of our future micro-processors. However, reliability challenges are also expected to increase at a high rate in near future. This graph now shows the expected contribution of different failure sources. Soft-errors in logic are among the major sources of in-field failures, which is the focus of work.

## Slide 3: Motivation
Overhead (perf., power, area)
Reliability
High reliability at low-cost
Redundancy

## Slide 4: SWAT: SoftWare Anomaly Treatment
Need handle only hardware faults that propagate to software
Fault-free case remains common, must be optimized
 Watch for software anomalies (symptoms)
    Zero to low overhead “always-on” monitors
Effective on SPEC, Server, and Media workloads
<1% µarch faults escape detectors and corrupt app output (SDC)
BUT, Silent Data Corruption rate is not zero
Fatal Traps
Kernel Panic
Hangs
App Abort
Out of Bounds

## Slide 5: Motivation
Redundancy
Overhead (perf., power, area)
Reliability
How?
Tunable
reliability
SWAT
Very high
reliability at low-cost
Goals:
Full reliability at low-cost
Systematic resiliency evaluation
Tunable reliability vs. overhead

## Slide 6: Fault Outcomes
APPLICATION
.
.
.
Output
Fault-free
execution
Masked
APPLICATION
.
.
.
Output
Transient Fault
e.g., bit 4 in R1
Faulty executions
APPLICATION
.
.
.
Output
Symptom detectors (SWAT):
Fatal traps, assertion violations, etc.
Symptom of Fault
Detection
Transient fault
again in bit 4 in R1

## Slide 7: Fault Outcomes
APPLICATION
.
.
.
Output
Fault-free
execution
Masked
APPLICATION
.
.
.
Output
APPLICATION
.
.
.
Output
Symptom of Fault
APPLICATION
.
.
.
Output
X
Detection
SDC
Faulty executions
Silent Data
Corruption (SDC)
SDCs are worst of all outcomes
How to eliminate SDCs?

## Slide 8: Approach
New detectors + selective duplication = Tunable resiliency at low cost
Find SDC causing application sites [ASPLOS 2012]
Detect at low cost [DSN 2012]
APPLICATION
.
.
Relyzer
APPLICATION
.
Comprehensive
resiliency analysis,
96% accuracy
APPLICATION
.
SDC-causing
fault
APPLICATION
.
Error Detection
Program-level Error Detectors
84% SDCs detected at 10% cost
Selective duplication for rest
~5 Years
for one app
<2 days
for one app

## Slide 9: Relyzer: Application Resiliency Analyzer
APPLICATION
.
.
.
Output
Pruning fault sites
Application-level error equivalence
Insight: Similar error propagation  similar outcome
Example:
Predict fault outcomes
Equivalence
Classes
Representatives
CFG
Errors in X that take paths behave similarly
X

## Slide 10: Relyzer Contributions [ASPLOS 2012]
Relyzer: A complete application resiliency analysis technique
Developed novel fault pruning techniques
  3 to 6 orders of magnitude fewer injections for most apps
  99.78% app fault sites pruned
    Only 0.004% represent 99% of all fault sites
Can identify all potential SDC causing fault sites
APPLICATION
.
.
Output
Relyzer
APPLICATION
.
.
Output

## Slide 11: SDC-targeted Program-level Detectors
SDC-hot app sites
Detectors only for SDC-vulnerable app locations
Challenge: Where to place detectors and what detectors to use?
Where: Many SDC-causing errors propagate to few program values
What (detectors): Test program-level properties
Array a, b;
For (i=0 to n) {
a[i] = b[i] + a[i]
}
C Code
A, B = base addr. of a, b
L: load r1, r2 ← [A], [B]
store r3 → [A]
. .
add A = A + 0x8
add B = B + 0x8
add i = i + 1
branch (i<n) L
ASM Code
All errors propagate here in few quantities
What: Property checks on A, B, and i
Diff in A = Diff in B
Diff in A = 8 Diff in i
Collect initial values
of A, B, and i
Example:

## Slide 12: Contributions [DSN 2012]
Discovered common program properties around most SDC-causing sites
Devised low-cost program-level detectors
  Avg. SDC reduction of 84% @ 10% avg. cost
New detectors + selective duplication = Tunable resiliency at low-cost
Chart: Average SDC Reduction
Relyzer + new detectors + selective duplication
Relyzer + selective duplication
18%
90%
24%
99%

## Slide 13: Other Contributions
APPLICATION
Output
mSWAT [Hari et al., MICRO’09]
Symptom detectors on Multicore systems
Novel diagnosis to isolate faulty core
Detection
Time
Checkpointing and rollback
I/O intensive apps
Latency-recoverability
Diagnosis
Recovery
Accurate fault modeling
FPGA validation of SWAT detectors [Pellegrini et al., DATE’12]
Gate-µarch-level simulator [Li et al., HPCA’09]
Complete Resiliency
Solution
Siva Hari (shari2@illinois.edu)
University of Illinois at Urbana-Champaign

## Slide 14: Backup

## Slide 15: Identifying Near Optimal Detectors: Naïve Approach
Bag of detectors
SDC coverage
SFI
50%
Example: Target SDC coverage = 60%
Sample 1
Overhead = 10%
Sample 2
Overhead = 20%
SFI
65%
Tedious and time consuming

## Slide 16: Identifying Near Optimal Detectors: Our Approach
Bag of detectors
Selected Detectors
SDC Covg.= X%
Overhead = Y%
Detector
1. Set attributes, enabled by Relyzer
2. Dynamic programming
Constraint: Total SDC covg. ≥ 60%
Objective: Minimize overhead
Overhead = 9%
Obtained SDC coverage vs. Performance trade-off curves [DSN’12]