## Slide 1
Preserving Application Reliability
on Unreliable Hardware
Siva Hari
Adviser: Sarita Adve
Department of Computer Science
University of Illinois at Urbana-Champaign

## Slide 2: Technology Scaling and Reliability Challenges
Nanometers
Increase (X)
*Source: Inter-Agency Workshop on HPC Resilience at Extreme Scale
hosted by NSA Advanced Computing Systems, DOE/SC, and DOE/NNSA, Feb 2012
Chart: 
| 2008 | 2010 | 2012 | 2014 | 2016 | 2018 | 2020
Technology | 45 | 32 | 22 | 14 | 10 | 7 | 5
Chart: 
| 2008 | 2010 | 2012 | 2014 | 2016 | 2018 | 2020
Technology | 45 | 32 | 22 | 14 | 10 | 7 | 5
Reliability challenges | 0 | 4 | 6.3 | 9.6 | 14.9 | 24.6 | 42.9

## Slide 3: Technology Scaling and Reliability Challenges
Nanometers
Increase (X)
Chart: 
| 2008 | 2010 | 2012 | 2014 | 2016 | 2018 | 2020
Technology | 45 | 32 | 22 | 14 | 10 | 7 | 5
Reliability challenges | 0 | 4 | 6.3 | 9.6 | 14.9 | 24.6 | 42.9
SER Mem | 0 | 1 | 1 | 1 | 1 | 1 | 1
SER Logic | 0 | 1 | 2 | 4 | 8 | 16 | 32
Variability | 0 | 1 | 1.3 | 1.6 | 1.9 | 2.1 | 2.4
Aging | 0 | 1 | 2 | 3 | 4 | 5.5 | 7.5
*Source: Inter-Agency Workshop on HPC Resilience at Extreme Scale
hosted by NSA Advanced Computing Systems, DOE/SC, and DOE/NNSA, Feb 2012
Hardware Reliability Challenges are for Real!
Sun experienced soft-errors in flagship enterprise server line, 2000
  America Online, eBay, and others were affected
Several documented in-field errors
  LANL Q Supercomputer: 27.7 failures/week from soft errors, 2005
  LLNL BlueGene/L experienced parity errors every 8 hours, 2007
Exascale systems are expected to fail every 35-40 minutes

## Slide 4: Motivation
Overhead (performance, power, area)
Hardware Reliability
High reliability at low-cost
Redundancy

## Slide 5: SWAT: A Low-Cost Reliability Solution
Need handle only hardware errors that propagate to software
Error-free case remains common, must be optimized
 Watch for software anomalies (symptoms)
    Zero to low overhead “always-on” monitors
Effective on SPEC, Server, and Media workloads
<0.6% µarch errors escape detectors & corrupt application output (SDC)
Fatal Traps
Division by zero,
RED state, etc.
Kernel Panic
OS enters panic
state due to error
Hangs
Simple HW hang
detector
App Abort
App abort due
to error
Out of Bounds
Flag illegal addresses

## Slide 6: Motivation
Redundancy
Overhead (performance, power, area)
Hardware Reliability
How?
Tunable
reliability
SWAT
Very high
reliability at low-cost
Goals:
Full reliability at low-cost
Systematic reliability evaluation
Tunable reliability vs. overhead
Notes: Goals for transient faults

## Slide 7: Error Outcomes
APPLICATION
.
.
.
Output
Error-free
execution
Masked
APPLICATION
.
.
.
Output
Faulty executions
APPLICATION
.
.
.
Output
Symptom detectors (SWAT):
Fatal traps, assertion violations, etc.
Symptom of error
Detection
Transient error
again in bit 4 in R1
Transient error,
Single bit flip
e.g., bit 4 in R1
APPLICATION
.
.
.
Output
X
SDC
Silent Data
Corruption (SDC)

## Slide 8: Error Outcomes
APPLICATION
.
.
.
Output
SDC
SDCs are worst of all outcomes
Examples
            Blackscholes: Computes prices of options
              23.34 → 1.33
              65,000 values were incorrect
            Libquantum: Factorizes 33 = 3 X 11
              Unable to determine factors
            LU: Matrix factorization
              RMSE = 45,324,668
How to convert SDCs to detections?
Ray Tracing
Notes: Remember the connection between recoverability and detection latency

## Slide 9: Approach
Finding all SDC-causing application-sites
Speeding up error simulations
APPLICATION
.
.
Output
Complete application
reliability evaluation
Challenge: Analyze all errors with few injections
Impractical, too many injections
>1,000 compute-years for one app
Relyzer: Prune Errors
APPLICATION
.
.
Output
Traditional approach:
Statistical Error Injections?
One injection at a time
APPLICATION
.
.
.
Output
Masked
or SDC?
mvEqualizer: Shorten by comparing state for equivalence
Challenge: Error simulations are time consuming
APPLICATION
.
.

## Slide 10: Advantages of Finding SDC-causing Sites
Convert SDCs to Detections at low cost
Evaluate simple program metrics to find SDCs
  Can simple metrics find SDCs without error injections?
    Example: lifetime, fan-out
APPLICATION
.
.
Output
SDC-causing error
APPLICATION
.
Error Detection
Error Detectors
Naïve approach:
Duplicate SDC-causing code locations
Our approach
 Relyzer enables such evaluations

## Slide 11: Contributions (1/3) [ASPLOS’12, Top Picks’13]
Relyzer: A complete application reliability analyzer for transient errors
  Developed novel error pruning techniques
99.78% error sites pruned for our applications, error models
  Only 0.004% represent 99% of all application error sites
Injections only in remaining sites  SDCs from virtually all app sites
APPLICATION
.
.
Output
Relyzer
APPLICATION
.
.
Output
Notes: Identified >99% SDCs for our apps, error models
=> Comprehensively analyze pin point SDCs in virtually all applications sites

## Slide 12: Contributions (2/3) [In review]
mvEqualizer: Speed up Relyzer by shortening full error simulations
  Compare simulation states repeatedly to show equivalence
  Leveraged program structure to identify when and what to compare
Only 36% require full application simulation for our workloads
  94% of saved simulations required execution of only 2,850 instructions
APPLICATION
.
.
.
Output
APPLICATION
.
.
Masked
or SDC?
APPLICATION
.
.
. . .
Injection 1
Injection 2
Injection n

## Slide 13: Contributions (3/3)
Convert identified SDCs to detections [DSN’12]
  Devised low cost program-level detectors
  84% SDCs reduced on average at 10% average execution overhead
    Selective duplication for rest
Tunable reliability at low cost [DSN’12]
  Found near optimal detectors for any SDC target
  Lower cost than pure duplication at all SDC targets
    E.g., 12% vs. 30% @ 90% SDC reduction
Evaluating simple metrics to find SDCs [in review, led by Venkatagiri]
  Found little correlation with SDC-causing instruction
   Relyzer + mvEqualizer is much needed
Chart: SDC reduction
Instr. duplication
Our approach
18%
90%

## Slide 14: Other Contributions
APPLICATION
Output
Time
Complete Reliability
Solution
Error
Accurate error modeling
FPGA-based [DATE’12]
Gate-µarch-level simulator [HPCA’09]
Detection
Multicore detection & diagnosis [MICRO’09]
Diagnosis
Checkpointing and rollback Handling I/O
Recovery

## Slide 15: Outline
Motivation
Relyzer: Application reliability analysis
mvEqualizer: Speeding up Relyzer
Applications of Relyzer:
  Converting SDCs to detections
  Tunable Reliability
  Evaluating simple metrics for finding SDCs
Summary and limitations
Next

## Slide 16: Relyzer: Application Reliability Analyzer
APPLICATION
.
.
.
Output
Prune error sites
Application-level error equivalence
Predict error outcomes
Injections for remaining sites
Equivalence Classes
Pilots
Relyzer
APPLICATION
.
.
Output
Can find SDCs from virtually all application sites

## Slide 17: Methodology for Relyzer
Pruning
  12 applications (from SPEC 2006, Parsec, and Splash 2)
Error model
  When (application) and where (hardware) to inject transient errors
  When: Every dynamic instruction that uses these units
  Where: Hardware error sites
    Errors in integer architectural registers
    Errors in output latch of address generation unit
  Single bit flip, one error at a time
Notes: Since the focus is on application level error analysis, we selected 2 hardware error sites in this study. In particular, we selected single bit flips in integer registers and output latch of the address generation unit. Faults in these hardware units are considered whenever that unit is unitized by the application.

## Slide 18: Pruning Results
99.78% of error sites are pruned
3 to 6 orders of magnitude pruning for most applications
  For mcf, two store instructions observed low pruning (of 20%)
Overall 0.004% error sites represent 99% of total error sites
Chart: % of all error sites
| Blackscholes | Fluidanimate | Streamcluster | Swaptions | FFT | LU | Ocean | Water | GCC | Libquantum | Mcf | Omnet++ | Total | Parsec 2.1 | Splash 2 | SPEC 2006 |
Remaining | 0.99996 | 0.9991 | 0.99992 | 0.99999 | 0.99999 | 0.99997 | 0.99987 | 0.99994 | 0.99875 | 0.99985 | 0.99427 | 0.99998 | 0.99781

## Slide 19: Outline
Motivation
Relyzer: Application reliability analysis
mvEqualizer: Speeding up Relyzer
  Error simulation framework
  Evaluation
Applications of Relyzer:
  Converting SDCs to detections
  Tunable Reliability
  Evaluating simple metrics for finding SDCs
Summary and limitations
Next

## Slide 20: mvEqualizer: Motivation
Relyzer is practical with 72 hrs of running time for 8 applications
65% of time is spent in error injections
Relyzer
.
.
.
Error sites in different dynamic instances of one static instruction
Error sites from pruned
instances of an instruction
.
.
mvEqualizer
.
.
Error sites in different instructions in a block
Error sites that need full application execution
Reducing full
app executions

## Slide 21: Challenges in Reducing Full Executions
Error simulations are time-consuming
  Run until output is produced
Aim: Shorten simulations
  Compare state for masking & similar corruptions
What to compare?
  Complete full system state (registers + memory)?
How frequently?
  Comparisons can be expensive
APPLICATION
.
.
.
Output
Masked or SDC?

## Slide 22: Approach: Fast Simulation Framework
Leverage program structure: SESE (single-entry-single-exit) regions*
  All data will flow through the exit point
SESE regions
Control-flow edges
f
e
b
a
1
2
3
4
6
5
7
8
9
10
12
11
13
14
15
16
c
*R. Johnson et al. The program structure tree: computing control regions in linear time. SIGPLAN Not., 1994

## Slide 23: Approach: Fast Simulation Framework
Leverage program structure: SESE (single-entry-single-exit) regions*
  All data will flow through the exit point
  Check for corruption in limited state (live registers + touched memory)
SESE regions
Control-flow edges
1
2
3
4
6
5
7
8
9
10
12
11
13
14
15
16
f
e
b
a
c
SESE Region
Other instructions
a
b
e
c
6
3
5
f
15
11
9
Program Structure Tree (PST)
*R. Johnson et al. The program structure tree: computing control regions in linear time. SIGPLAN Not., 1994

## Slide 24: Error Simulation Algorithm
SESE exit 1
SESE exit 2
SESE exit 3
Start from a system checkpoint
Injection 1
Injection 2
Group error sites to check for equivalence
Typical group size in our framework was 100-1000
State for comparison:
(live) processor registers
+
touched memory locations
(stored incrementally from the
starting point of the group)
Start of a group
.
.
.
All injection runs start from the beginning of a group

## Slide 25: Error Simulation Algorithm
SESE exit 1
SESE exit 2
SESE exit 3
Start from a system checkpoint
Injection 1
Injection 2
Injection 3
X
X
X
X
=
=
Group error sites to check for equivalence
Only one error injection needs full simulation in this example
Start of a group
.
.
.

## Slide 26: Methodology for mvEqualizer
Eight applications from Parsec and SPLASH2
Error model: single bit flips in integer architectural registers at every dynamic instruction
Employed after Relyzer
Implemented in architecture simulator (Simics)

## Slide 27: Efficacy of mvEqualizer
Chart: Fraction of error injection simulations
| Blackscholes | Fluidanimate | Streamcluster | Swaptions | FFT | LU | Ocean | Water | Average
Detected | 11754 | 48799 | 9369 | 38043 | 9717 | 8195 | 140281 | 42049 | 38525.875
Saved | 21786 | 73186 | 11052 | 41935 | 10160 | 11950 | 127630 | 68526 | 45778.125
Need Full | 6044 | 50840 | 9972 | 29461 | 15021 | 11722 | 214090 | 45389 | 47817.375
Only 36% of error sites need full simulations
36%
35%
29%

## Slide 28: Savings from Equalized Simulations
Chart: Fraction of simulations equalized at Nth SESE exit
| Average
1 | 0.93971
2 | 0.054934
3 | 0.0053528
Chart: Average distance to Nth SESE exit (only for saved simulations)
| Average
1 | 2868.451
2 | 18944.0857
3 | 16245.5571
94% of equalized simulations require 2,850 instructions to be executed

## Slide 29: Outline
Motivation
Relyzer: Application reliability analysis
mvEqualizer: Speeding up Relyzer
Applications of Relyzer:
  Converting SDCs to detections
    Program-level detectors
    Evaluation
  Tunable Reliability
  Evaluating simple metrics for finding SDCs
Summary and limitations
Next

## Slide 30: Converting SDCs to Detections: Our Approach
Challenges:
Where to place?
What to use?
Uncovered error-sites?
Approach:
: Many errors propagate to few program values
  End of loops and function calls
: Test program-level properties
  E.g., comparing similar computations, value equality
: Selective instruction-level duplication
APPLICATION
.
.
Output
SDC-causing
error
APPLICATION
.
Error Detectors
Error Detection

## Slide 31: SDC-Causing Code Properties
Loop incrementalization
Registers with long life
Application-specific behavior

## Slide 32: Categorization of SDC-causing Sites
Categorized >88% SDC-causing sites
Chart: % SDCs
| Blackscholes | FFT | Libquantum | LU | Swaptions | Water
Registers with long life | 10.5795 | 6.9234 | 48.8608 | 11.2881 | 0.73993 | 14.3507
Incrementalized loops | 11.8789 | 46.8113 | 41.9375 | 81.5356 | 4.5703 | 28.6771
App specific | 76.4548 | 34.7807 | 0 | 0 | 91.4624 | 46.7264
Uncovered | 1.0868 | 11.4845 | 9.2017 | 7.1762 | 3.2274 | 10.2458
Added Lossless Detectors
Added Lossy
Detectors

## Slide 33: Efficacy of Detectors
84% average SDC reduction at 10% average overhead
Chart: SDC Reduction
| Average
SDC Reduction | 0.83
Chart: Execution Overhead
| Average
Execution overhead | 0.102

## Slide 34: Tunable Reliability
What if our low-overhead is still not tolerable but lower reliability is?
  Tunable reliability vs. overhead
Need to find a set of optimal-cost detectors at any given SDC target

## Slide 35: Tunable Reliability: Challenges
Naïve approach
Bag of detectors
50% SDC
reduction
SFI
Example: Target SDC reduction = 60%
Sample 1
Overhead = 10%
Sample 2
Overhead = 20%
Challenges:
  Repeated statistical error injections  time consuming
  Do not know detectors’ contribution in reducing SDCs a priori
(program-level +
duplication-based)
SFI
65% SDC
reduction

## Slide 36: Identifying Near Optimal Detectors: Our Approach
Bag of detectors
Selected Detectors
SDC Red.= X%
Overhead = Y%
Detector
1. Set attributes, enabled by Relyzer
2. Dynamic programming
Constraint: Total SDC red. ≥ 60%
Objective: Minimize overhead
Overhead = 9%
Obtained SDC reduction vs. Performance trade-off curves
Relyzer lists SDC-causing sites, number of SDCs these sites produce
 Knowledge of SDCs covered by each detector
(program-level + duplication-based)

## Slide 37: SDC Reduction vs. Overhead Trade-off Curve
Selective duplication
Chart: SDC Reduction

## Slide 38: SDC Reduction vs. Overhead Trade-off Curve
Program-level detectors provide lower cost solutions
Our detectors +
selective duplication
Selective duplication
Chart: SDC Reduction
18%
90%
24%
99%

## Slide 39: Outline
Motivation
Relyzer: Application reliability analysis
mvEqualizer: Speeding up Relyzer
Applications of Relyzer:
  Converting SDCs to detections
  Tunable Reliability
  Evaluating simple metrics for finding SDCs
Summary and limitations
Next

## Slide 40: Evaluating Program Analysis Based Metrics
Relyzer requires significant time to obtain applications’ resiliency profile
  Expensive input specific program analyses
  Error injection experiments
Can simple metrics find SDCs?
Prior approach to predict error detections
  Lifetime (average, aggregate) per instruction
  Fanout (average, aggregate) per instruction
  Dynamic instruction count
Evaluating these for SDCs is tedious
 Relyzer enables this evaluation
Wi
Wi
Ri
Ri
Lifetime
Wi
Ri
Ri . . .
Ri
Fanout = number of reads

## Slide 41: Evaluation Methodology
Five applications from Parsec and SPLASH2
Error model: single bit flips in destination integer architectural registers
Collected metric information using architectural simulator (Simics)
Direct correlation of simpler metrics with Relyzer
Compare effectiveness of detectors added by Relyzer vs. simpler metrics
Combination of simpler metrics
  Linear
  Linear combination on polynomials

## Slide 42: Results: Simple Metrics are Non-trivial (1/2)
Lifetime (agg) | Fanout (agg) | Lifetime (av) | Fanout (av) | Dyn. Inst.
Poor (< 0.31) | Poor-Fair (0.12 – 0.59) | Poor (< 0.08) | Poor (< 0.04) | Poor-Good (0.18 – 0.82)
Correlation coefficient between metrics and Relyzer
Comparing the effectiveness of adding duplication based detectors
Chart: LU: fanout
Chart: LU: fanout
Chart: LU: fanout
LU: Fanout (agg) (Corr. Coeff. = 0.59)
Relyzer
Predicted coverage of detectors selected using metric
Actual coverage of
detectors selected
using metric
Significant difference

## Slide 43: Results: Simple Metrics are Non-trivial (2/2)
Only 7% – 68% variance in SDCs can be explained by linear combination
  26% – 79% for linear combination of polynomials
  No common model explains SDCs for our workloads
Unable to adequately predict an instruction’s vulnerability to SDCs
   Relyzer + mvEqualizer is much needed
% SDCs Covered
% dynamic instructions for duplication (cost)
LU: Dyn. Inst. (Corr. Coeff. = 0.82)
% SDCs Covered
% dynamic instructions for duplication (cost)
FFT: Dyn. Inst. (Corr. Coeff. = 0.80)
Relyzer
Predicted for metric
Actual for metric
Significant difference

## Slide 44: Summary
Relyzer: Novel error pruning for reliability analysis [ASPLOS’12, TopPicks’13]
  3 to 6 orders of magnitude fewer injections for most applications
  Identified SDCs from virtually all applications sites
mvEqualizer: Reducing error injection time
  Only 36% remaining error sites need full application simulation
Applications of Relyzer (+ mvEqualizer)
  Devised low cost program-level detectors [DSN’12]
    84% average SDC reduction at 10% average cost
  Tunable reliability at low cost [DSN’12]
    Obtained SDC reduction vs. performance trade-off curves
  Evaluated simpler program analyses based metrics
    Finding a simpler metric is hard  Relyzer is valuable
Other contributions: Multicore detection and diagnosis [MICRO’09], Accurate error modeling [DATE’12, HPCA’09], Checkpointing and rollback

## Slide 45: Limitations and Future Directions
Relyzer
  More (multithreaded) applications and error models
  Obtaining input independent reliability profiles
Detectors
  Automating detectors’ placement and derivation
  Developing app independent, failure-source-oblivious detectors
Designing inherently error resilient programs
Detection latency and recoverability
Application-aware SDC categorization

## Slide 46
Thank You

## Slide 47: Backup

## Slide 48: Related Work

## Slide 49: iSWAT vs. Our Work
iSWAT [DSN’08] | Our Work
Permanent errors | Transient errors
Range-based likely invariants on stores | Broad range of detectors
Suffers from false positives | No false positives
Combining insights for both error models is interesting future direction

## Slide 50: Pattabiraman et al. vs. Our Work
Our Work | Pattabiraman et al. [EDDC’06, PRDC’05]
Goal: Reduce SDCs | Avoid crashes, limit error propagation
Relyzer [ASPLOS’12] identifies SDC-causing app sites | Lifetime, fanout identify vulnerable variables [PRDC’05]
Property checks involve multiple variables | Tests do not consider other variables
No false positives | Suffers from false positives

## Slide 51: SymPLFIED vs. Relyzer
Similar goal of finding SDCs
Symbolic execution to abstract erroneous values
  Performs model checking with abstract execution technique
Reduces the number of injections per application site
  Relyzer reduces the number of applications sites
  Relyzer restricts the injections/app site by selecting few error models
Combining SymPLFIED and Relyzer would be interesting

## Slide 52: Shoestring vs. Relyzer
Our Work | Shoestring
Static + dynamic program analyses | Pure static analysis Finds short-enough data paths to the symptom generating instructions
Detection mechanism: Program-level property checks | Instruction-level duplication
Combining Shoestring and Relyzer would be interesting
Similar goal: Finding and reducing SDCs

## Slide 53: Relyzer

## Slide 54: Store Equivalence
Insight: Errors in stores may be similar if stored values are used similarly
Heuristic to determine similar use of values:
  Same number of loads use the value
  Loads are from same PCs
Store
Memory
PC1
PC2
Load
Load
Store
PC1
PC2
Load
Load
Instance 1
Instance 2
PC
PC

## Slide 55: Pruning Predictable Errors
Prune out-of-bounds accesses
  Detected by symptom detectors
  Memory addresses not in &
Boundaries obtained by profiling
Reserved
Stack
Reserved
Heap
Data
Text
SPARC Address Space Layout
0x0
0x100000000
0x80100000000
0xfffff7ff00000000
0xffffffffffbf0000

## Slide 56: Definition to First-Use Equivalence
Error in first use is equivalent to error in definition  prune definition
  Error model: single bit flips in operands, one error at a time
  r1 = r2 + r3
  r4 = r1 + r5
  …
If there is no first use, then definition is dead  prune definition
Definition
First use

## Slide 57: Control Flow Equivalence
  Insight: Errors flowing through similar control paths may behave similarly*
CFG
X
Errors in X that take paths behave similarly
Heuristic: Use direction of next 5 branches
  *Errors in stores are handled differently

## Slide 58: Methodology: Validating Pruning Techniques
PILOTS
SAMPLE
Validation for Control and Store equivalence pruning
APPLICATION
.
.
.
Output
Compute Prediction Rate
Equivalence
Classes

## Slide 59: Validating Pruning Techniques
Validated control and store equivalence
  >2M injections for randomly selected pilots, samples from equivalent set
96% combined accuracy (including fully accurate prediction-based pruning)
99% confidence interval with <5% error
Chart: Average Prediction Rate
| Reg - Control | Reg - Store | Agen - Control | Agen - Store | Combined
Average | 0.95682 | 0.95395 | 0.94523 | 0.9264 | 0.96026

## Slide 60: Potential Impact of Relyzer
Relyzer, for the first time, finds SDCs from virtually all program locations
SDC-targeted error detectors
  Placing detectors where needed
  Designing application-centric detectors
Tuning reliability at low cost
  Balancing reliability vs. performance
Designing inherently error resilient programs
  Why do certain errors remain silent?
  Why do errors in certain code sequences produce more detections?

## Slide 61: mvEqualizer

## Slide 62: Significance of Comparing Live Processor State
Chart: Fraction of error injection simulations
| All registers | Live registers
Detected | 39093.125 | 38525.875
Saved | 33309 | 45778.125
Need Full | 60800.125 | 47817.375
46%
25%
29%
36%
35%
29%
40% more equalizations occurred when live state was compared

## Slide 63
More comparison points may yield better simulation time savings
Chart: 
| Blackscholes | Fluidanimate | Streamcluster | Swaptions | FFT | LU | Ocean | Water | Average
Reg Only | 3032 | 24052 | 4551 | 10544 | 3275 | 2443 | 32344 | 14716 | 11869.625
Mem Only | 47 | 529 | 184 | 1771 | 1623 | 678 | 21977 | 3099 | 3738.5
Reg+Mem | 1682 | 15636 | 2178 | 13533 | 7338 | 3284 | 70327 | 14265 | 16030.375
Timeouts | 1283 | 10626 | 3060 | 3613 | 2785 | 5380 | 89475 | 13371 | 16199.125
Fraction of unsaved (need full) simulations

## Slide 64: Detectors

## Slide 65: Loop Incrementailzation
A = base addr. of a
B = base addr. of b
L: load r1 ← [A]
. . .
load r2 ← [B]
. . .
store r3 → [A]
. . .
add A = A + 0x8
add B = B + 0x8
add i = i + 1
branch (i<n) L
Array a, b;
For (i=0 to n) {
. . .
a[i] = b[i] + a[i]
. . .
}
C Code
ASM Code

## Slide 66: Loop Incrementailzation
A = base addr. of a
B = base addr. of b
L: load r1 ← [A]
. . .
load r2 ← [B]
. . .
store r3 → [A]
. . .
add A = A + 0x8
add B = B + 0x8
add i = i + 1
branch (i<n) L
Array a, b;
For (i=0 to n) {
. . .
a[i] = b[i] + a[i]
. . .
}
C Code
ASM Code
Where: Errors from all iterations propagate here in few quantities
What: Property checks on A, B, and i
Diff in A = Diff in B
Diff in A = 8 Diff in i
Collect initial values of A, B, and i
SDC-hot app sites

## Slide 67: Registers with Long Life
Some long lived registers are prone to SDCs
For detection
  Duplicate the register value at its definition
  Compare its value at the end of its life
Life
time
R1 definition
Copy
Use 1
Compare
Use 2
Use n
.
.
.

## Slide 68: Application-Specific Behavior
Exponential function
  Where: End of every function invocation
  What: Re-execution or inverse function (log)
  Periodic test on accumulated quantities
  Accumulate input and output with and
Other detectors: Range checks
Some coverage may be compromised – lossy
exp
exp
few
s

## Slide 69: Application-Specific Behavior
Bit Reverse function
  Where: End of function
  What: Challenge – re-execution?
  Approach: Parity of in & out should match
Other detectors: Range checks
Some coverage may be compromised – lossy
Bit Reverse
Compare
Parity
Parity

## Slide 70: Methodology for Detectors
Six applications from SPEC 2006, Parsec, and SPLASH2
Error model: single bit flips in integer architectural registers at every dynamic instruction
Ran Relyzer, obtained SDC-causing sites, examined them manually
Our detectors
  Implemented in architecture simulator
  Overhead estimation: number of assembly instructions needed

## Slide 71: SDC Reduction
84% average SDC reduction (67% - 92%)
Chart: SDC Reduction
| Blackscholes | FFT | Libquantum | LU | Swaptions | Water | Average
Lossless | 0.22458 | 0.53735 | 0.90798 | 0.92824 | 0.053102 | 0.43028 | 0.51359
Lossy | 0.64408 | 0.25221 | 0 | 0 | 0.61653 | 0.42931 | 0.32369

## Slide 72: Execution Overhead
10% average overhead (0.1% - 18%)
Chart: Execution Overhead
| Blackscholes | FFT | Libquantum | LU | Swaptions | Water | Average
Lossless | 1.6586e-06 | 0.077648 | 0.00079089 | 0.12571 | 0.0448 | 0.053963 | 0.050486
Lossy | 0.17627 | 0.084192 | 1e-08 | 1e-08 | 0.010426 | 0.035133 | 0.051003

## Slide 73: Tunable Reliability: Challenges
Naïve approach
Bag of detectors
50% SDC
reduction
SFI
Example: Target SDC reduction = 60%
Sample 1
Overhead = 10%
Sample 2
Overhead = 20%
Challenges:
  Repeated statistical error injections  time consuming
  Do not know detectors’ contribution in reducing SDCs a priori
(program-level +
duplication-based)
SFI
65% SDC
reduction

## Slide 74: Regressions
Linear combination
Linear combination of polynomials

## Slide 75
Chart: LU: fanout

## Slide 76: SDC Examples
Blackscholes
  4.13125 → 4.12999
  23.33927 → 1.33247
  65,000 values were incorrect
Libquantum: Factorizes 33 to 11 x 3
  Impossible measurement
  Unable to determine factors
LU
  RMSE = 217781729.775298
  RMSE = 45324667.7812618

## Slide 77: Hardware vs. Software Errors
Statistics across LANL systems [Schroeder et al. SciDAC 2007]