## Slide 1
Preserving Application Reliability
on Unreliable Hardware
Siva Hari
Department of Computer Science
University of Illinois at Urbana-Champaign

## Slide 2: Technology Scaling and Reliability Challenges
Nanometers
Increase (X)
*Source: Inter-Agency Workshop on HPC Resilience at Extreme Scale
hosted by NSA Advanced Computing Systems, DOE/SC, and DOE/NNSA, Feb 2012
Chart: 
| 2008 | 2010 | 2012 | 2014 | 2016 | 2018 | 2020
Technology | 45 | 32 | 22 | 14 | 10 | 7 | 5
Chart: 
| 2008 | 2010 | 2012 | 2014 | 2016 | 2018 | 2020
Technology | 45 | 32 | 22 | 14 | 10 | 7 | 5
Reliability challenges | 0 | 4 | 6.3 | 9.6 | 14.9 | 24.6 | 42.9

## Slide 3: Technology Scaling and Reliability Challenges
Nanometers
Increase (X)
Chart: 
| 2008 | 2010 | 2012 | 2014 | 2016 | 2018 | 2020
Technology | 45 | 32 | 22 | 14 | 10 | 7 | 5
Reliability challenges | 0 | 4 | 6.3 | 9.6 | 14.9 | 24.6 | 42.9
SER Mem | 0 | 1 | 1 | 1 | 1 | 1 | 1
SER Logic | 0 | 1 | 2 | 4 | 8 | 16 | 32
Variability | 0 | 1 | 1.3 | 1.6 | 1.9 | 2.1 | 2.4
Aging | 0 | 1 | 2 | 3 | 4 | 5.5 | 7.5
*Source: Inter-Agency Workshop on HPC Resilience at Extreme Scale
hosted by NSA Advanced Computing Systems, DOE/SC, and DOE/NNSA, Feb 2012
Hardware Reliability Challenges are for Real!
Sun experienced soft-errors in flagship enterprise server line, 2000
  America Online, Ebay, and others were affected
Several documented in-field errors
  LANL Q Supercomputer: 27.7 failures/week from soft errors, 2005
  LLNL BlueGene/L experienced parity errors every 8 hours, 2007
Exascale systems are expected to fail every 35-40 minutes

## Slide 4: Motivation
Overhead (performance, power, area)
Hardware Reliability
High reliability at low-cost
Redundancy

## Slide 5: SWAT: A Low-Cost Reliability Solution
Need handle only hardware faults that propagate to software
Fault-free case remains common, must be optimized
 Watch for software anomalies (symptoms)
    Zero to low overhead “always-on” monitors
Effective on SPEC, Server, and Media workloads
<0.5% µarch faults escape detectors and corrupt application output (SDC)
Can we bring silent data corruptions (SDCs) to zero?
Fatal Traps
Division by zero,
RED state, etc.
Kernel Panic
OS enters panic
state due to fault
Hangs
Simple HW hang
detector
App Abort
App abort due
to fault
Out of Bounds
Flag illegal addresses

## Slide 6: Motivation
Redundancy
Overhead (performance, power, area)
Hardware Reliability
How?
Tunable
reliability
SWAT
Very high
reliability at low-cost
Goals:
Full reliability at low-cost
Systematic reliability evaluation
Tunable reliability vs. overhead
Notes: Goals for transient faults

## Slide 7: Fault Outcomes
APPLICATION
.
.
.
Output
Fault-free
execution
Masked
APPLICATION
.
.
.
Output
Faulty executions
APPLICATION
.
.
.
Output
Symptom detectors (SWAT):
Fatal traps, assertion violations, etc.
Symptom of Fault
Detection
Transient fault
again in bit 4 in R1
Transient fault,
Single bit flip
e.g., bit 4 in R1

## Slide 8: Fault Outcomes
APPLICATION
.
.
.
Output
Fault-free
execution
Masked
APPLICATION
.
.
.
Output
APPLICATION
.
.
.
Output
Symptom of Fault
APPLICATION
.
.
.
Output
X
Detection
SDC
Faulty executions
Silent Data
Corruption (SDC)
SDCs are worst of all outcomes
Examples
            Blackscholes: Computes prices of options
              23.34 → 1.33
              65,000 values were incorrect
            Libquantum: Factorizes 33 = 3 X 11
              Unable to determine factors
            LU: Matrix factorization
              RMSE = 45,324,668
How to convert SDCs to detections?
Ray Tracing
Notes: Remember the connection between recoverability and detection latency

## Slide 9: Approach
Find all SDC-causing application-sites
Convert SDCs to Detections
APPLICATION
.
.
Output
APPLICATION
.
.
Output
SDC-causing fault
APPLICATION
.
Error Detection
Error Detectors
Challenges:
What detectors to use?
Where to place?
Complete application
reliability evaluation
Challenge: Analyze all faults with few injections
Impractical, too many injections
>1,000 compute-years for one app
Relyzer: Prune Faults
APPLICATION
.
.
Output
Traditional approach:
Statistical Fault Injections?
Duplicate SDC-producing values?
One injection at a time

## Slide 10: Contributions (1/2) [ASPLOS’12, Top Picks’13]
Relyzer: A complete application reliability analyzer for transient faults
  Developed novel fault pruning techniques
99.78% fault sites pruned for our applications, fault models
  Only 0.004% represent 99% of all application fault sites
Identified SDCs from virtually all applications sites
APPLICATION
.
.
Output
Relyzer
APPLICATION
.
.
Output
Notes: Identified >99% SDCs for our apps, fault models
=> Comprehensively analyze pin point SDCs in virtually all applications sites

## Slide 11: Contributions (2/2) [DSN’12]
Convert identified SDCs to detections
  Discovered common program properties for SDC-causing sites
  Devised low cost program-level detectors
84% SDCs reduced on average at 10% average execution overhead
  Selective duplication for rest
Tunable reliability at low cost
  Found near optimal detectors for any SDC target
  Lower cost than pure duplication at all SDC targets
    E.g., 12% vs. 30% @ 90% SDC reduction
Chart: SDC reduction
Instr. duplication
Our approach
18%
90%

## Slide 12: Other Contributions
APPLICATION
Output
Time
Complete Reliability
Solution
Fault
Accurate fault modeling
FPGA-based [DATE’12]
Gate-µarch-level simulator [HPCA’09]
Detection
Multicore detection & diagnosis [MICRO’09]
Diagnosis
Checkpointing and rollback
Handling I/O
Recovery

## Slide 13: Outline
Motivation
Relyzer: Complete application reliability analysis
Converting SDCs to detections
Tunable Reliability
Summary and future directions

## Slide 14: Outline
Motivation
Relyzer: Complete application reliability analysis
  Pruning techniques
  Evaluation methodology
  Results
Converting SDCs to detections
Tunable Reliability
Summary and future directions

## Slide 15: Relyzer: Application Reliability Analyzer
APPLICATION
.
.
.
Output
Prune fault sites
Application-level fault equivalence
Predict fault outcomes
Injections for remaining sites
Equivalence Classes
Pilots
Relyzer
APPLICATION
.
.
Output
Can find SDCs from virtually all application sites

## Slide 16: Definition to First-Use Equivalence
Fault in first use is equivalent to fault in definition  prune definition
  Fault model: single bit flips in operands, one fault at a time
  r1 = r2 + r3
  r4 = r1 + r5
  …
If there is no first use, then definition is dead  prune definition
Definition
First use

## Slide 17: Control Flow Equivalence
  Insight: Faults flowing through similar control paths may behave similarly*
CFG
X
Faults in X that take paths behave similarly
Heuristic: Use direction of next 5 branches
  *Faults in stores are handled next

## Slide 18: Store Equivalence
Insight: Faults in stores may be similar if stored values are used similarly
Heuristic to determine similar use of values:
  Same number of loads use the value
  Loads are from same PCs
Store
Memory
PC1
PC2
Load
Load
Store
PC1
PC2
Load
Load
Instance 1
Instance 2
PC
PC

## Slide 19: Pruning Predictable Faults
Prune out-of-bounds accesses
  Detected by symptom detectors
  Memory addresses not in &
Boundaries obtained by profiling
Reserved
Stack
Reserved
Heap
Data
Text
SPARC Address Space Layout
0x0
0x100000000
0x80100000000
0xfffff7ff00000000
0xffffffffffbf0000

## Slide 20: Methodology for Relyzer
Pruning
  12 applications (from SPEC 2006, Parsec, and Splash 2)
Fault model
  When (application) and where (hardware) to inject transient faults
  When: Every dynamic instruction that uses these units
  Where: Hardware fault sites
    Faults in integer architectural registers
    Faults in output latch of address generation unit
  Single bit flip, one fault at a time
Notes: Since the focus is on application level fault analysis, we selected 2 hardware fault sites in this study. In particular, we selected single bit flips in integer registers and output latch of the address generation unit. Faults in these hardware units are considered whenever that unit is unitized by the application.

## Slide 21: Pruning Results
99.78% of fault sites are pruned
3 to 6 orders of magnitude pruning for most applications
  For mcf, two store instructions observed low pruning (of 20%)
Overall 0.004% fault sites represent 99% of total fault sites
Chart: % of all fault sites
| Blackscholes | Fluidanimate | Streamcluster | Swaptions | FFT | LU | Ocean | Water | GCC | Libquantum | Mcf | Omnet++ | Total | Parsec 2.1 | Splash 2 | SPEC 2006 |
Remaining | 0.99996 | 0.9991 | 0.99992 | 0.99999 | 0.99999 | 0.99997 | 0.99987 | 0.99994 | 0.99875 | 0.99985 | 0.99427 | 0.99998 | 0.99781

## Slide 22: Methodology: Validating Pruning Techniques
PILOTS
SAMPLE
Validation for Control and Store equivalence pruning
APPLICATION
.
.
.
Output
Compute Prediction Rate
Equivalence
Classes

## Slide 23: Validating Pruning Techniques
Validated control and store equivalence
  >2M injections for randomly selected pilots, samples from equivalent set
96% combined accuracy (including fully accurate prediction-based pruning)
99% confidence interval with <5% error
Chart: Average Prediction Rate
| Reg - Control | Reg - Store | Agen - Control | Agen - Store | Combined
Average | 0.95682 | 0.95395 | 0.94523 | 0.9264 | 0.96026

## Slide 24: Potential Impact of Relyzer
Relyzer, for the first time, finds SDCs from virtually all program locations
SDC-targeted error detectors
  Placing detectors where needed
  Designing application-centric detectors
Tuning reliability at low cost
  Balancing reliability vs. performance
Designing inherently error resilient programs
  Why do certain errors remain silent?
  Why do errors in certain code sequences produce more detections?

## Slide 25: Outline
Motivation
Relyzer: Complete application reliability analysis
Converting SDCs to detections
  Program-level detectors
  Evaluation methodology
  Results
Tunable Reliability
Summary and future directions

## Slide 26: Converting SDCs to Detections: Our Approach
Challenges:
Where to place?
What to use?
Uncovered fault-sites?
Approach:
: Many errors propagate to few program values
  End of loops and function calls
: Test program-level properties
  E.g., comparing similar computations, value equality
: Selective instruction-level duplication
APPLICATION
.
.
Output
SDC-causing
fault
APPLICATION
.
Error Detectors
Error Detection

## Slide 27: SDC-Causing Code Properties
Loop incrementalization
Registers with long life
Application-specific behavior

## Slide 28: Loop Incrementailzation
A = base addr. of a
B = base addr. of b
L: load r1 ← [A]
. . .
load r2 ← [B]
. . .
store r3 → [A]
. . .
add A = A + 0x8
add B = B + 0x8
add i = i + 1
branch (i<n) L
Array a, b;
For (i=0 to n) {
. . .
a[i] = b[i] + a[i]
. . .
}
C Code
ASM Code

## Slide 29: Loop Incrementailzation
A = base addr. of a
B = base addr. of b
L: load r1 ← [A]
. . .
load r2 ← [B]
. . .
store r3 → [A]
. . .
add A = A + 0x8
add B = B + 0x8
add i = i + 1
branch (i<n) L
Array a, b;
For (i=0 to n) {
. . .
a[i] = b[i] + a[i]
. . .
}
C Code
ASM Code
Where: Errors from all iterations propagate here in few quantities
What: Property checks on A, B, and i
Diff in A = Diff in B
Diff in A = 8 Diff in i
Collect initial values of A, B, and i
SDC-hot app sites

## Slide 30: Registers with Long Life
Some long lived registers are prone to SDCs
For detection
  Duplicate the register value at its definition
  Compare its value at the end of its life
Life
time
R1 definition
Copy
Use 1
Compare
Use 2
Use n
.
.
.

## Slide 31: Application-Specific Behavior
Exponential function
  Where: End of every function invocation
  What: Re-execution or inverse function (log)
  Periodic test on accumulated quantities
  Accumulate input and output with and
Other detectors: Range checks
Some coverage may be compromised – lossy
exp
exp
few
s

## Slide 32: Methodology for Detectors
Six applications from SPEC 2006, Parsec, and SPLASH2
Fault model: single bit flips in integer architectural registers at every dynamic instruction
Ran Relyzer, obtained SDC-causing sites, examined them manually
Our detectors
  Implemented in architecture simulator
  Overhead estimation: number of assembly instructions needed
Lossy detectors’ coverage
  Statistical fault injections (10,000)

## Slide 33: Categorization of SDC-causing Sites
Categorized >88% SDC-causing sites
Chart: % SDCs
| Blackscholes | FFT | Libquantum | LU | Swaptions | Water
Registers with long life | 10.5795 | 6.9234 | 48.8608 | 11.2881 | 0.73993 | 14.3507
Incrementalized loops | 11.8789 | 46.8113 | 41.9375 | 81.5356 | 4.5703 | 28.6771
App specific | 76.4548 | 34.7807 | 0 | 0 | 91.4624 | 46.7264
Uncovered | 1.0868 | 11.4845 | 9.2017 | 7.1762 | 3.2274 | 10.2458
Added Lossless Detectors
Added Lossy
Detectors

## Slide 34: SDC Reduction
84% average SDC reduction (67% - 92%)
Chart: SDC Reduction
| Blackscholes | FFT | Libquantum | LU | Swaptions | Water | Average
Lossless | 0.22458 | 0.53735 | 0.90798 | 0.92824 | 0.053102 | 0.43028 | 0.51359
Lossy | 0.64408 | 0.25221 | 0 | 0 | 0.61653 | 0.42931 | 0.32369

## Slide 35: Execution Overhead
10% average overhead (0.1% - 18%)
Chart: Execution Overhead
| Blackscholes | FFT | Libquantum | LU | Swaptions | Water | Average
Lossless | 1.6586e-06 | 0.077648 | 0.00079089 | 0.12571 | 0.0448 | 0.053963 | 0.050486
Lossy | 0.17627 | 0.084192 | 1e-08 | 1e-08 | 0.010426 | 0.035133 | 0.051003

## Slide 36: Outline
Motivation
Relyzer: Complete application reliability analysis
Converting SDCs to detections
Tunable Reliability
Summary and future directions

## Slide 37: Tunable Reliability
What if our low-overhead is still not tolerable but lower reliability is?
  Tunable reliability vs. overhead
Need to find a set of optimal-cost detectors at any given SDC target

## Slide 38: Tunable Reliability: Challenges
Naïve approach
Bag of detectors
50% SDC
reduction
SFI
Example: Target SDC reduction = 60%
Sample 1
Overhead = 10%
Sample 2
Overhead = 20%
Challenges:
  Repeated statistical fault injections  time consuming
  Do not know detectors’ contribution in reducing SDCs a priori
(program-level +
duplication-based)
SFI
65% SDC
reduction

## Slide 39: Identifying Near Optimal Detectors: Our Approach
Bag of detectors
Selected Detectors
SDC Red.= X%
Overhead = Y%
Detector
1. Set attributes, enabled by Relyzer
2. Dynamic programming
Constraint: Total SDC red. ≥ 60%
Objective: Minimize overhead
Overhead = 9%
Obtained SDC reduction vs. Performance trade-off curves
Relyzer lists SDC-causing sites, number of SDCs these sites produce
 Knowledge of SDCs covered by each detector
(program-level + duplication-based)

## Slide 40: SDC Reduction vs. Overhead Trade-off Curve
Selective duplication
Chart: SDC Reduction

## Slide 41: SDC Reduction vs. Overhead Trade-off Curve
Program-level detectors provide lower cost solutions
Our detectors +
selective duplication
Selective duplication
Chart: SDC Reduction
18%
90%
24%
99%

## Slide 42: Summary
Relyzer: Novel fault pruning for reliability analysis [ASPLOS’12, TopPicks’13]
  3 to 6 orders of magnitude fewer injections for most applications
  Identified SDCs from virtually all applications sites
Devised low cost program-level detectors [DSN’12]
  84% average SDC reduction at 10% average cost
Tunable reliability at low cost
  Obtained SDC reduction vs. performance trade-off curves
  Lower cost than pure duplication: 12% vs. 30% @ 90% SDC reduction
Other contributions:
  Multicore detection and diagnosis [MICRO’09]
  Accurate fault modeling [DATE’12, HPCA’09]
  Checkpointing and rollback

## Slide 43: Future Directions
Automating detectors’ placement and derivation
Developing app independent, failure-source-oblivious detectors
  More (parallel, server) applications
  More fault models: µarch/gate-level, permanent, un-core components
Obtaining input independent reliability profiles
Designing inherently error resilient programs
Detection latency and recoverability
Emerging platforms have diverse reliability demands
  Application-aware error tolerance, approximate computation
  Holistic view  balancing reliability, energy, & cost budgets
Ubiquitous Sensors
(Data collection)
Portable Devices
(Analysis)
Cloud Servers
(Processing)

## Slide 44
Thank You

## Slide 45: Backup

## Slide 46: iSWAT vs. Our Work
iSWAT [DSN’08] | Our Work
Permanent faults | Transient Faults
Range-based likely invariants on stores | Broad range of detectors
Suffers from false positives | No false positives
Combining insights for both fault models is interesting future direction

## Slide 47: Pattabiraman et al. vs. Our Work
Our Work | Pattabiraman et al. [EDDC’06, PRDC’05]
Goal: Reduce SDCs | Avoid crashes, limit error propagation
Relyzer [ASPLOS’12] identifies SDC-causing app sites | Lifetime, fanout identify vulnerable variables [PRDC’05]
Property checks involve multiple variables | Tests do not consider other variables
No false positives | Suffers from false positives

## Slide 48: SymPLFIED vs. Relyzer
Similar goal of finding SDCs
Symbolic execution to abstract erroneous values
  Performs model checking with abstract execution technique
Reduces the number of injections per application site
  Relyzer reduces the number of applications sites
  Relyzer restricts the injections/app site by selecting few fault models
Combining SymPLFIED and Relyzer would be interesting

## Slide 49: Shoestring vs. Relyzer
Our Work | Shoestring
Static + dynamic program analyses | Pure static analysis Finds short-enough data paths to the symptom generating instructions
Detection mechanism: Program-level property checks | Instruction-level duplication
Combining Shoestring and Relyzer would be interesting
Similar goal: Finding and reducing SDCs

## Slide 50: Application-Specific Behavior
Bit Reverse function
  Where: End of function
  What: Challenge – re-execution?
  Approach: Parity of in & out should match
Other detectors: Range checks
Some coverage may be compromised – lossy
Bit Reverse
Compare
Parity
Parity

## Slide 51: SDC Examples
Blackscholes
  4.13125 → 4.12999
  23.33927 → 1.33247
  65,000 values were incorrect
Libquantum: Factorizes 33 to 11 x 3
  Impossible measurement
  Unable to determine factors
LU
  RMSE = 217781729.775298
  RMSE = 45324667.7812618

## Slide 52: Future Directions
Emerging applications have diverse reliability demands
  Personalized healthcare, market analysis, etc.
Leverage inherent application error-tolerance
  Holistic view  balancing reliability, energy, & cost budgets
Data collection → Processing → Analysis
Ubiquitous Sensors
Portable Devices
Cloud Servers